## Slide 1: Real-time magnetospheric simulation on GOCE decay
Tiera Laitinen1, Ilja Honkonen1,2, Minna Palmroth1, Pekka Janhunen1
1) Finnish Meteorological Institute
2) NASA/GSFC

## Slide 2: Outline
GOCE decay and re-entry
GUMICS
  The only European global magnetosphere-ionosphere simulation model
  Real-time capable parallel version GUMICS-5
Space weather effects in GOCE decay
  Increase in the decay rate during space weather events
  Decay rate variations are well reproduced by GUMICS simulation and a simple atmospheric density perturbation model.

## Slide 4: GOCE re-entry
Ran out of propellant 21 Oct 2013.
Re-entered atmosphere 11 Nov near Falkland.
Re-entry gained wide media attention also in Finland.
FMI launched a campaign to test real-time modelling of space weather effects on GOCE orbit.
FMI supported Geodetic Institute in informing Finnish authorities on the satellite (LUOVA warnings)
Information was also provided to ESA SSA/SST (debris surveillance and tracking)

## Slide 5: Space weather during GOCE decay
There were no major storms, but moderate geomagnetic disturbances occurred.
The most interesting was 30 October.

## Slide 6
Real-time space weather modelling

## Slide 7: GUMICS
Global magnetosphere-ionosphere coupling simulation model
The only one of its kind in Europe
Developed at FMI since 1993
Dozens of scientific publications
MHD magnetosphere
Electrostatic ionosphere

## Slide 8: GUMICS: magnetosphere

## Slide 9
GUMICS: ionosphere
6.11.2014
9

## Slide 10: GUMICS: M-I-coupling
Solar wind
J‖
e– prec.
Φ
Mapped along dipole field lines:
B, n, T, v, …
Φ, Σ, J, E, e– prec., …

## Slide 11: GUMICS-5
A new parallel version of the code
  Currently under validation and finalisation.
Capable of faster than real time running
  with moderate resolution, ~ 0.5 - 1 RE
  requires ~ 100 cores.
First technical real time operations test was performed during the GOCE case

## Slide 12: Chained run system
Solar wind propagation from L1 takes ~ 1 h.
Allows ~ 20 min prediction time.
Initial state from the previous run
Latest solar wind from ACE
Run extended beyond
measured solar wind with constant input
New run every 20 min

## Slide 13: GUMICS results
Real-time simulations were done with GUMICS-5.
Later the period was simulated with GUMICS-4 with better resolution.
Joule heating + electron precipitation.
Integral over 24 h (heat accumulation).

## Slide 14
From Joule heating to air drag

## Slide 15: A toy model for heat deposition
Height [km]
Extra heat
from SWE
Temperature change
Quiet time atmospheric profiles from NRLMSISE-00
JH from GUMICS
Assume globally even heat distribution
Assume heating profile with maximum at 120 km

## Slide 16: Density increases above ~130 km
Atmospheric profiles without and with ionospheric heating
Pressure
Density
Temperature
Height [km]
Height [km]
Height [km]

## Slide 17: Extracting changes in decay rate
Nominal decay rate in a time-invariant atmosphere
Real decay rate
Space weather effect?
Decay rate [km/orbit]
Nominal density at orbit from NRLMSISE-00
Fit to the real decay rate (get air drag coefficient)
  Fitted density is the nominal decay rate
Calculate difference of real and nominal decay rate

## Slide 18: Simulation predicts orbit variations

## Slide 19: Conclusions & discussion
Global MHD simulation predicts variations in GOCE decay rate.
This analysis was done afterwards, but the procedure could be implemented as a forecast routine (with forecast time ~ 20 min).
The forecast time could be lengthened with solar wind data from
  a measurement sunward of L1
  an accurate solar wind simulation.