## Slide 1: A New Solar Observing Network For Space Weather Operations & Solar Physics Research
Frank Hill, NSO, USA
Markus Roth, KIS, Germany
Michael J Thompson, HAO, USA
ESWW10, Antwerp
Nov. 19, 2013

## Slide 2: What and Why a Network
No substitute for “complete” temporal and spatial observations of the Sun
Ground-based network (a set of geographically distributed identical instruments) is proven strategy for this
Network is not as vulnerable to space weather as a space platform
Network is 10-15 times less expensive than space platforms
Network can be maintained and upgraded for very long time periods
Network provides continual context for large telescope operations

## Slide 3: An existing network: GONG
Operating since 1995
Two instruments:
  Michelson Interferometer
    helioseismology Doppler velocity, intensity and LOS magnetic field
    1k x 1k full-disk images in Ni I 676.8 nm
    60-sec cadence
  AFWA-funded filter system
    H- intensity
    2k x 2k full-disk images
    60-sec cadence at a given site, 20-sec cadence from network

## Slide 5
Duty Cycle red<0.5 yellow< 0.7 green>0.82 median=0.91
NSO/GONG Udaipur
H Intensity
2012/02/14
These images are returned in near-real time and are available on the Internet

## Slide 6: Space Weather Products from GONG
Far-side helioseismic maps every 12 hours
  Used by NOAA/SWPC
Magnetic field
  10-min average & variance
  Synoptic magnetic field map & PFSS coronal field extrapolation from ~8000 magnetograms every hour
  Used by NOAA/SWPC for solar wind and geomagnetic storm forecasts
  Used by NASA/CCMC
H- intensity every 20 sec around the clock
  Used by US Air Force Weather Agency

## Slide 9
GONG H-
June 6, 2011
GONG Web sites:
Top level: gong.nso.edu
Synoptic maps & PFSS:
gong.nso.edu/data/magmap
gong.nso.edu/data/magmap/pfss.html
Farside: farside.nso.edu
H-: halpha.nso.edu

## Slide 10: SPRING
Solar Physics Research Integrated Network Group
Multi-wavelength ground-based network to replace GONG and SOLIS
Provide multi-height data for helioseismology, vector magnetometry, irradiance variations and space weather operations
Workshop April 22-24 in Boulder, hosted by HAO
  40 participants from all areas, including radio and coronal physics, and space missions
  Meeting report published in Space Weather, 11, 392
Many science drivers
Work package of SOLARNET, KIS lead

## Slide 11: Science requirements
Full-disk Doppler velocity, vector magnetic field images, and intensity images -> Stokes
Variety of wavelengths
Cadence of no longer than 60 seconds
Spatial resolution of 1” (0.5” pixels)
90% duty cycle
25 year lifetime
Velocity sensitivity: 1 m/s /pixel /image (?)
Magnetic field sensitivity: 5 G /pixel /image (?)

## Slide 12: New Network Concept
Multi-instrument platform
Flexibility at each site
Mission-specific instruments, fewer compromises

## Slide 13: Possible instrument concepts
Filtergraph
Spectrograph
Interferometer

## Slide 14: Next steps (2014-2017)
Meeting next week in Freiburg
Develop SRD, TRD
Evaluate instrument concepts
Select two or three for testing
Develop next step proposal
Cost estimates: Development – construction - operations